## Slide 1: Project_NUI Natural User Interface
Realization of a motion tracking system to control navigation and selection in a QlikView application deployed on a Browser

## Slide 2
QLIKVIEW
KINECT
POSSIBLE ACTIONS IN QLIKVIEW
SOFTWARE ARCHITECTURE
OVERVIEW
DETAILED VIEW
TECHNICAL ARCHITECTURE
BEHAVIOR OF AN ACTION / A GESTURE : CHAIN OF REPONSIBILITY
FINGER DETECTION
WEB CLIENT
ARCHITECTURE
UI
INSTALLATION AND USE
ISSUES & FEATURES
ANNEXES

## Slide 7
TECHNICAL SOLUTIONS ?

## Slide 8
CRITERIA\CHOICES | KINECT | WEBCAM | LEAP ?
PRICE | 250$ | 30€ | 70$
DEV DURATION | Body: 2w, Fingers: 3w, Voice: 2w, | Body: 4w , Fingers: 4w, Voice: ? | ?
COVER REQUIREMENTS | Full | No Voice | No Voice
EXECUTION TIME | ++ | + | ?
SUSTAINABILITY | + | ++ | ?
NEEDED | Kinect SDK + OpenCV | OpenCV | ?
PROS | Native detection of the skeleton + micros | Present everywhere | innovation
CONS | High cost ? | Hard to implement the detection | Not available before decembre 2012
PROBLEMATIC | Making a motion detection system to control navigation and selection in a QlikView application through a Browser

## Slide 10
KINECT SENSORS
IR Emitter
Color Sensor
IR Depth Sensor
Tilt Motor
Microphone Array

## Slide 11
KINECT DATAS
Skeleton datas
Sound datas
Depth datas

## Slide 12
POSSIBLE ACTIONS IN QLIKVIEW

## Slide 13
Action | PC controller | Body controller | Visual FeedBack
Unique selection | Mouse left click | Hand Forward / Fingers down | Circle
Multiple Selection | Click maintained Ctrl + click | Left Fist + Unique selection / Voice + Unique Selection | Circle
Menu | Right Click |  | 
Elevator | Mouse Wheel | Fingers / Vertical Waves | 
Clear | Btn | ‘Clear’ | Eraser
Next/Previous | Btn | ‘Next’/’Previous’ | Arrow
Change Tab | Btn | Horizontal Wave | /
Add a bookmark | Btn | Voice | Star +
Delete a bookmark | Btn | Voice | Star -
Select a bookmark | Btn | Voice | Star
Create a note | Btn | Voice | /
Close/Home | Btn | ‘Close’ | /
Search | Btn | Voice | 
Zoom/UnZoom | Ctrl+ Mouse Wheel | ‘Max’/’Min’ - Hands in diagonal | /
Navigation (Object+Sheet) | Mouse | 1 hand steady + 1 hand moving | Cursor [+ skeleton]

## Slide 14
SOFTWARE ARCHITECTURE
OVERVIEW

## Slide 15
Kinect
Web Client
Gesture and Voice Detection
Web Connector
API javascript
Mouse + KeyBoard
Hardware Connector
Manager
instantiates
event
others
stream

## Slide 16
SOFTWARE ARCHITECTURE
DETAILED VIEW

## Slide 17
QlikMoveManager
KinectHelper
GestureHelper
VoiceHelper
ActionHelper
SkeletonReady()
DepthReady()
AudioStream
InitKinect()
EventRecognised()
EventRecognised()
ActionRecognised()
SocketServer
Send()
OurAPI
Receive()
Dispatch()
QvAjax
Method()
Kinect
MouseSimulator
SetPosition()
Input()
Cursor
X
y
Web Client
instantiates
event
others
stream

## Slide 18
BEHAVIOUR OF AN ACTION/ A GESTURE
CHAIN OF RESPONSABILITY

## Slide 19
1
Event (Body/Hand/Voice)
ACTION
Action
ActionPart1
ActionPart2
CheckPart()
ActionPart++
CheckPart()
ACTION VALIDATED
ActionHelper
ACTION PART :
0
1
2
1
2
* nbActions
List<Actions> Actions
Queue<Event> Events
Actions.UpdateAll(Events)

## Slide 20
TECHNICAL ARCHITECTURE

## Slide 21
Web-Socket.js
OurAPI.js
QvAjax.js
WEB CLIENT
Microsoft.Kinect.dll
Microsoft.Recognition + System.Speech.Recognition
Body_Gesture_Recognition.cs
Emgu.dll
Hand_Gesture_
Recognition.cs
Fleck.dll
user32.dll
(mouse controler)
+

## Slide 22
FINGER DETECTION

## Slide 23
HAND DETECTOR
NIVEAU A0
skeletonFrame
depthFrame
handType
Template classes
Emgu.CV
FoundTemplateDesc*2
List of templates
Class Name
handtype
Contour
description
all_Frames_Ready

## Slide 24
LEVEL A-0
CheckMovement()
GetEverything
Between(min,max)
ExtractContourAndHull()
GetNearestClass()
Skeleton
Frame
Depth
Frame
HandType
CheckOrientation()
R
E
S
U
L
T
S
Emgu.CV
Template Classes
Hand Detector
CheckZHand()
All
Frames
Ready

## Slide 25
WEB CLIENT
ARCHITECTURE

## Slide 26
Socket server
onMessage()
MsgManager
message
QvAjaxInterface
CallQvAjax()
UIManager
datas
UI1
datas
UI2
datas
UI3
datas
Server
Send()
message
Kinect
Action
Skeleton
Audio
context
context
context
json
Currently we are mixing the QvAjax and Jquery triggers on buttons

## Slide 27
At the moment the scripts are deployed as an extension
Including all the scripts and styles

## Slide 28
WEB CLIENT
UI

## Slide 29
ELEMENTS | DETAILS
Kinect state | Light
Skeleton state | Distance Viewer
Joints | Canvas sticks
Voice state | Graduate Volume
Finger Tracking | /
Hand Position | Cursor
Shape of the Hand | Cursor
Performed action | Text + picture

## Slide 30
Deploy/Undeploy icon
Minimize
Maximize
Kinect State Viewer
Volume Viewer
Distance Viewer
SkeletonViewer
ActionViewer
Visual Feedback
s

## Slide 31
Selection Cursor
(when the circle is filled, the element passes to selected)
Current selected QvFrame
This allow specified action related to the element : scroll, clear, etc..

## Slide 32
INSTALLATION & USE

## Slide 33
Install the Kinect runtime 1.6
Double click on the extension and copy paste in the server
Install the QlikView.Move
Launch/ refresh the client
Use
The software will change the z-angle automatically – during this phase you won’t be recognised
When you will be recognised, the web UI will show up if you are viewing a web QlikView app – when you leave it will undeploy
Another user can come and take control by raising his hands in the air
Libs | Link
Kinect Runtime v1.6 (containing the drivers ) | http://www.microsoft.com/en-us/kinectforwindows/develop/developer-downloads.aspx
emgucv-windows-x86 2.3.0.1416 | http://www.emgu.com/wiki/index.php/Download_And_Installation
Fleck.dll | https://github.com/statianzo/Fleck/
opencv_core231.dll | 
opencv_imgproc231.dll | 

## Slide 34
A log file is created in the application folder.
log info : 14:41:44
16/08/2012 14:41:44 [INFO] | QlikMove ==> Init QlikMove
16/08/2012 14:41:44 [INFO] | BodyGestureControler ==> BodyGestures defined
16/08/2012 14:41:44 [INFO] | HandGestureControler ==> HandGestures defined
16/08/2012 14:41:44 [INFO] | VoiceHelper ==> Grammars loaded
16/08/2012 14:41:44 [INFO] | ActionHelper ==> Actions defined
16/08/2012 14:41:44 [INFO] | ServerHelper ==> Server initialized
16/08/2012 14:41:44 [INFO] | KinectHelper ==> Kinect Status : Connected
16/08/2012 14:41:48 [INFO] | VoiceHelper ==> audio stream started
16/08/2012 14:41:49 [INFO] | KinectHelper ==> skeleton is now tracked
16/08/2012 14:41:49 [INFO] | KinectHelper ==> tracking has lost the skeleton
16/08/2012 14:41:50 [INFO] | KinectHelper ==> Kinect sensor is moving
16/08/2012 14:41:51 [INFO] | KinectHelper ==> skeleton is now tracked
16/08/2012 14:42:20 [INFO] | ActionHelper ==> action Recognised :
Action type : PREVIOUS_TAB
timeStamp : 16 August 2012
List of the events :
Event type : BODY
timeStamp : 16/08/2012 14:42:20
16/08/2012 14:42:20 [INFO] | ActionHelper ==> current window file:///C:/Users/pce/Documents/Visual Studio 11/Projects/QlikMove/QlikMove/bin/Debug/QlikMove.EXE
16/08/2012 14:42:21 [INFO] | ActionHelper ==> action Recognised :
Action type : PREVIOUS_TAB
timeStamp : 16 August 2012
List of the events :
Event type : BODY
timeStamp : 16/08/2012 14:42:21

## Slide 35
ISSUES & POSSIBILITIES

## Slide 36
The finger detection is not accurate. We should limitate it to open/close detection or implement a learning machine if we want more (predator TLD)
WebSockets are not already supported by all browsers
A visual software could be implemented so that the user could create his own movements and link them with actions based on a database + see his actual movements
The current software should be transformed to a service if we do not want any configuration from the user.
Create an installer

## Slide 37
ANNEXES

## Slide 38
Got a problem

## Slide 39
CRITERIA\CHOICES | NUGGET.dll | FLECK.dll | SUPERSOCKET.dll | .NET
EASY TO HANDLE | + | + + | - | - -
SUSTAINABILITY | + | + | + + | + +
COVER REQUIREMENTS | + | + | + | +
DEV DURATION | + | + + | - | - -
PROBLEMATIC | Conduct a dialogue interface between a server. NET and a web client interchanging text data